OFC Line Cable

| APPLICATIONS | FEATURES |
| --- | --- |
| Electric Instruments Hi-Fi Interconnects Test Probers Audio Patch Cords AMP to Cabinet Leads | Stays Flexible even in Sub-Zero Weather Oxygen Free Copper Conductor & Shield Reduced Microphonic Handling Noise Low Capacitance & Resistance |

GS-6

A specially designed Oxygen Free Copper 18 AWG cable for connecting Guitar/Bass or Keyboards to amps, mixers, effects pedals and all outboard signal processing gear. Low capacitance and low series resistance provides improved frequency response (flat to 50KHz). A bright, ringing characteristic sound is preserved, even when using Hi-Z guitar picking with long cable runs. The proprietary double Carbon/Braid Copper shield construction eliminates microphonic handling noise, especially on stage where amps are often set at maximum volume levels.

| Model | Sales units | Nom. O.D | Weight | Inner cond. | Insula -tion | Outer Cond. | Electrical characteristics |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Cross sec area (AWG) and cond. comp. | Nom. O.D | Nom. O.D | Shield construction and coverage | Ch. D.C.R. | Shield. D.C.R. | Nom. cap. * |
|  | m | mm | kg/100m | mm²/(AGW) Q'ty/mm | mm | mm | mm/ends/ carriers | ��/100m | ��/100m | pF/m |
| GS-6 | 100 200 | 5.8 | 5.0 | 1.0(18) 127/0.1(OFC) | 1.3 | 3.0 | Carbon plastic shield +0.1(OFC)/ 8/16 92% or more | 1.8 | 2.5 | 160 |

Jacket: PVC. *Capacitance between conductors

GS-4, GS-6

OFC outer conductor of fine 0.1mm�� strands provide a highly flexible braided configuration.

OFC center conductor with 127 fine 0.1mm�� strands (50 for GS-4) increases durability.

Important wiring note

Canare  GS-6 utilizes a specially designed Conductive Carbon Plastic Shield  to protect against undesirable microphonic handling noise. This inner sleeve can cause a short circuit if allowed to come in contact with the OFC center conductor. Please be very careful when stripping cable and remove this material from a exposed insulation before soldering.

After 80,000 bending test

Canare GS-6

Other Typical shielded line

Frequency Response for GS-6